## Slide 1
SMART IOT FIRE & SMOKE DETECTION SYSTEM
Early Warning & Automated Mitigation
Supervisor: Eng. Rahma Khaled

## Slide 2
INTRODUCTION & PROBLEM STATEMENT
The Problem
Fire and smoke accidents pose significant risks to lives and property.
Delayed detection often leads to catastrophic consequences.
Traditional alarms lack remote monitoring and automated ventilation.
▹
▹
▹
The Solution
An integrated IoT system for early warning and mitigation.
Real-time sensor fusion using ESP32 and multi-point sensing.
Automated response including fans, buzzers, and web alerts.
▹
▹
▹

## Slide 3
SYSTEM ARCHITECTURE OVERVIEW
Input Layer
Sensors gather environmental data
(flame, gas, temperature) and send it to
the ESP32.
Processing Layer
ESP32 analyzes sensor fusion data
against safety thresholds to determine
system state.
Output Layer
Automated triggers activate actuators
and update the real-time web dashboard.

## Slide 4
HARDWARE COMPONENTS & DESIGN
Control
ESP32 DevKit V1
Dual-core CPU, Wi-Fi stack, and GPIO management.
Sensing
Flame Sensors (x5)
IR-based detection for 360° fire monitoring.
Sensing
MQ-2 Gas Sensor
Analog detection of smoke and LPG concentrations.
Sensing
DS18B20 Sensor
OneWire digital temperature monitoring.
Actuation
DC Fan & L298N
PWM-controlled ventilation for smoke extraction.
Interface
LCD 16x2 I2C
Real-time local data visualization and status.

## Slide 5
SYSTEM LOGIC & WORKFLOW
SYSTEM STATE
CONDITION & RESPONSE
SAFE
No fire or smoke detected.
▹ Green LED ON | Fan OFF | Buzzer OFF
WARNING
Low-level gas/smoke detected.
▹ Red LED ON | Fan LOW Speed | Buzzer OFF
DANGER
Fire or high smoke density detected.
▹ Red LED ON | Fan MAX Speed | Buzzer ON
The ESP32 executes this logic loop every 50ms, ensuring near-instantaneous response to environmental changes. Data is simultaneously pushed to the web dashboard via JSON.

## Slide 6
WEB MONITORING DASHBOARD
Real-Time Updates
Asynchronous fetching updates sensors every 2s without reload.
Responsive Interface
Mobile-first layout supports phones, tablets and desktops.
Cloud Ready
Exposes a compact JSON endpoint for easy IoT integration.
JSON DATA ENDPOINT
{
"fire"
:
true
,
"gasVal"
:
2450
,
"temp"
:
28.5
,
"motor"
:
255
,
"danger"
:
true
,
"status"
:
"ACTIVE"
}
Color-coded alerts: Green = safe, Red = emergency for immediate recognition.

## Slide 7
TESTING SCENARIOS & RESULTS
TEST SCENARIO
SYSTEM RESPONSE
STATUS
No Fire or Smoke
Normal state maintained; Green LED active.
PASS
Smoke Detected
Fan activated (Low); Red LED active; Warning on Web.
PASS
Fire Detected
Fan at MAX; Buzzer active; Danger alert on Web.
PASS
Instant Response — Flame sensors responded immediately.
Reliable Connectivity — Dashboard kept stable sync.
Sensor Accuracy — MQ-2 & DS18B20 consistent across cycles.
Fail-Safe Operation — System returned to safe state post-hazard.

## Slide 8
CONCLUSION & FUTURE SCOPE
Project Summary
Successfully developed a responsive IoT safety system using the ESP32 platform.
Integrated multi-sensor fusion for reliable fire, smoke, and temperature monitoring.
Implemented automated mitigation via ventilation fans and audible alarms.
Established a real-time web dashboard for remote monitoring and data access.
▹
▹
▹
▹
Future Enhancements
Cloud Integration: Implement Firebase or AWS IoT for long-term data logging and analytics.
Mobile Alerts: Add push notifications via Blynk or IFTTT for instant emergency updates.
Active Suppression: Integrate a relay-controlled water pump or CO2 release system.
AI Diagnostics: Use machine learning to predict fire risks based on historical sensor data.
▹
▹
▹
▹

## Slide 9
THANK YOU
Any Questions?
GitHub:
https://github.com/SarahGamalKotb/Fire-Smoke-Detector-IOT
Portfolio:
http://10.250.7.121/
Email:
sarakotp44@gmail.com